## Slide 1: Number Systems
Seminar by Rhys Stever

## Slide 2: Bases
Base 10- Decimal (0, 1, 2, 3, 4, 5, 6, 7, 8, 9)
Base 2- Binary (0 and 1)
Base 8- Octal (0, 1, 2, 3, 4, 5, 6, 7)
Base 16- Hexadecimal (0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F)

## Slide 3: Binary
“Base 2”: 1 and 0

## Slide 4: Decimal  Binary
Take the starting number and divide it by 2
Write the remainder to the right (1 or 0)
Write how many times it was divided below it
Take the number in Step 3 and do repeat steps 1-3 until the number is 0
“Read Up” all of the remainders
Ex) Decimal Number: 17
2 / 17 1
2 / 8 0
2 / 4 0
2 / 2 0
2 / 1 1
0
Binary Equivalent:

## Slide 5: Binary  Decimal
Take each digit of the starting number and multiply it by , where n is the place value
Add up all of the numbers
Ex) Binary Number:
0 0 0 1
Decimal Equivalent: 17

## Slide 6: Octal
Octal | Binary
0 | 000
1 | 001
2 | 010
3 | 011
4 | 100
5 | 101
6 | 110
7 | 111
“Base 8”: 0, 1, 2, 3, 4, 5, 6, 7

## Slide 7: Decimal  Octal
Take the starting number and divide it by 8
Write the remainder to the right
Write how many times it was divided below it
Take the number in Step 3 and do repeat steps 1-3 until the number is 0
“Read Up” all of the remainders
Ex) Decimal Number: 99
8 / 99 3
8 / 12 4
8 / 4 1
0
Octal Equivalent:

## Slide 8: Octal  Decimal
Take each digit of the starting number and multiply it by , where n is the place value
Add up all of the numbers
Ex) Octal Number:
1 4 3
Decimal Equivalent: 99

## Slide 9: Binary  Octal
Break the binary number into sets of 3 digits
Convert each of those sets into octal digits
Put each digit together to form the octal number
Binary Number:
1 1 0 0 1 1
110 011
6 3
Octal Equivalent:

## Slide 10: Octal  Binary
Take each digit and convert it to binary (will be a 3-digit set)
Put each digit’s binary equivalent together to form the binary number
Octal Number:
6 3
110 011
Binary Equivalent:

## Slide 11: Hexadecimal
“Base 16”: 0, 1, 2, 3, 4, 5, 6, 7,
8, 9, A, B, C, D, E, F
Dec. | Hexa. | Binary | Dec. | Hexa. | Binary
0 | 0 | 0000 | 8 | 8 | 1000
1 | 1 | 0001 | 9 | 9 | 1001
2 | 2 | 0010 | 10 | A | 1010
3 | 3 | 0011 | 11 | B | 1011
4 | 4 | 0100 | 12 | C | 1100
5 | 5 | 0101 | 13 | D | 1101
6 | 6 | 0110 | 14 | E | 1110
7 | 7 | 0111 | 15 | F | 1111

## Slide 12: Decimal  Hexadecimal
Take the starting number and divide it by 16
Write the remainder to the right (*Remember to change any number 10-15 into the corresponding hexadecimal digit)
Write how many times it was divided below it
Take the number in Step 3 and do repeat steps 1-3 until the number is 0
“Read Up” all of the remainders
A = 10 D = 13
B = 11 E = 14
C = 12 F = 15
Ex) Decimal Number: 267
16 / 267 11  B
16 / 16 0
16 / 1 1
0
Hexadecimal Equivalent:

## Slide 13: Hexadecimal  Decimal
Take each digit of the starting number and multiply it by , where n is the place value
Add up all of the numbers
A = 10 D = 13
B = 11 E = 14
C = 12 F = 15
Ex) Hexadecimal Number:
1 0 B
Decimal Equivalent: 267

## Slide 14: Binary  Hexadecimal
Split the binary number up into sets of 4 digits
Convert each set into the corresponding hexadecimal digit
Put each hexadecimal digit together
Binary Number:
1 0 1 1 0 0 1 1
1011 0011
9 3
Hexadecimal Equivalent:

## Slide 15: Hexadecimal  Binary
Take each hexadecimal digit and convert it to its 4-digit binary equivalent
Put all of the 4-digit binary sets together
Hexadecimal Number:
9 3
1011 0011
Binary Equivalent:

## Slide 16: Octal  Hexadecimal
Convert the octal number into binary
Split the binary number up into sets of 4 digits
Convert each 4-digit set into the corresponding hexadecimal digit
Put all of the hexadecimal digits together
Hexadecimal Number:
3 0 3 2
101 000 101 010
1 0 1 0 0 0 1 0 1 0 1 0
1010 0010 1010
8 2 8
Octal Equivalent:

## Slide 17: Hexadecimal  Octal
Reverse of Octal  Hexadecimal
Convert each hexadecimal digit into binary
Put each 4-digit set together
Split the binary number into sets of 3 digits
Convert each 3-digit set into octal
Put each octal digit together
Hexadecimal Number:
8 2 8
1010 0010 1010
1 0 1 0 0 0 1 0 1 0 1 0
101 000 101 010
3 0 3 2
Octal Equivalent:

## Slide 18: Operators

## Slide 19: Addition

## Slide 20: Subtraction

## Slide 21: Multiplication

## Slide 22: Division